## Slide 1: Open Pyrojet – Graphical Assembly Manual
By Michael Thomas Lynn
maydraal@gmail.com

## Slide 2
Things we will need to get started:
• A desktop CNC router(I use the Genmitsu 3018 Pro with 0.1mm tip, 10 degree draft single flute router bits), band saw, hack saw, or jewelers saw.
• 2.54mm pitch perfboard, preferably high quality FR4 with nickel plated through vias.
• 1.27mm pitch perfboard, preferably high quality FR4 with nickel plated through vias.
• Alternatively, plain copper clad high quality FR4, less vias.
• A box of M1-M1.4 X 3mm self-tapping black oxide coated screws
• Silicon carbide monofilament, 0.14mm diameter or less, from any supplier. SCS-6(carbon core), goodfellow (tungsten core) or elsewhere will do.
• Basic Multimeter with resistance measuring capabilities between 20K Ohm and 1 Ohm.
• Kapton tape 1” wide or less
• Gorilla glue, or JB weld set clear, 2 part, foam free epoxy, or PMMA super glue
• 2.54 mm pitch male header pins color coded with at least 9 discrete colors.
• 0.015” diameter 32Sn64Pb4Ag flux core solder
• Fine tip 0.3-0.6mm diameter 10 degree draft, soldering iron tip(I find this to be easiest for me)
• Soldering iron
• Precision screw driver set, with fine point flat head, and fine point Phillips bits
• A flat and level work surface
• A good work light and magnifier (microscope camera, eye loop, head visor, soldering magnifier will do)
A hard flat sheet of fine grit sandpaper, or aluminum oxide sheet.
A fine tip sharpie.

## Slide 3
Things we will need to get started: Links to items
2.54mm perfboard : https://www.digikey.com/en/products/detail/bud-industries/EXN-23402-PCB/5886452
1.27mm perfboard : https://www.amazon.com/6x8CM-Double-Prototype-Perforated-Through/dp/B01LZA2UJZ
M1 self tapping screws :
https://www.amazon.com/Suit-JERLITU-Phillips-Multi-Purpose-Assortment-Self-Tapping/dp/B08V56GVR2/ref=sr_1_3?crid=29AXFL3H6JDX8&keywords=m1+phillips+head+micro+screws+self+tapping+wood+screws&qid=1645933611&s=industrial&sprefix=m1+phillips+head+micro+screws+self+tapping+wood+screw%2Caps%2C138&sr=1-3-catcorr
Silicon carbide Monofilament : https://www.specmaterials.com/silicon-carbide-fiber-product-price-list
https://www.goodfellow.com/us/en-us/displayitemdetails/p/si67-mt-000120/silicon-carbide-monofilament

## Slide 4
Preparing the Backplane
Lenox Hack Saw with medium metal blade
2.54mm pitch FR4 perfboard
1.Mill/saw out a rectangular piece of the 2.54mm perfboard, 11 holes long, by 5 holes wide. Approximately, 29 mm long, by 15 mm wide. Try to keep your cuts as straight as possible.

## Slide 5
Preparing the Backplane
29mmX15mm cut piece
2.54mm pitch FR4 perfboard
1.Mill/saw out a rectangular piece of the 2.54mm perfboard, 11 holes long, by 5 holes wide. Approximately, 29 mm long, by 15 mm wide. Try to keep your cuts as straight as possible.

## Slide 6
Preparing the Backplane
1.Mill/saw out a rectangular piece of the 2.54mm perfboard, 11 holes long, by 5 holes wide. Approximately, 29 mm long, by 15 mm wide. Try to keep your cuts as straight as possible.
29mmX15mm “Backplane”
Electrical contacts/inkfeed holes we will use

## Slide 7
Preparing the Backplane
2. Lap the rough cut edges of the back plane to make sure it will fit nicely on the nozzle plate. Be sure to dunk the backplane 99% IPA or a similar cleaning agent to remove dust and oil after lapping.
Al2O3 sheet for lapping
Backplane having it’s edges lapped smooth.

## Slide 8
Preparing the nozzle plate
3. Place the freshly cut, lapped and cleaned backplane onto the 1.27mm pitch perfboard, aligning the holes of each board.
Mark the position with a fine point sharpie, and mark the location of the heater row on the nozzle plate as well.
Fine point sharpie
1.27mm pitch perfboard (for nozzle plate)
Backplane
Heater Row

## Slide 9
Installing the heating element
4. Find your silicon carbide monofilament heating element of choice. Mine is a specialty materials, SCS-6 standard 0.135mm carbon core 3C, beta, silicon carbide CVD derived monofilament.
1.27mm pitch perfboard (for nozzle plate)
Backplane

## Slide 10
Installing the heating element
5. Just above where you made your heater row mark, place a piece of Kapton tape, being careful not to cover the row of holes in the 1.27mm perfboard where your heater row goes.
1.27mm pitch perfboard (for nozzle plate)
Kapton Tape
Heater Row

## Slide 11
Installing the heating element
6. Place another piece of Kapton along the bottom edge of the 1.27mm perfboard, just below your heater row mark as shown, to secure the nozzle plate to your work surface and provide alignment of the filament as well as preload between the nozzle plate and the backplane.
1.27mm pitch perfboard (for nozzle plate)
Kapton Tape
Heater Row
SiC Filament

## Slide 12
Installing the heating element
7. Lay the silicon carbide monofilament along the heater row as shown, between the pieces of Kapton tape.
1.27mm pitch perfboard (for nozzle plate)
Kapton Tape
SiC Filament

## Slide 13
Installing the heating element
8. Secure the filament to the 1.27mm pitch perfboard nozzle plate and across the heater row with Kapton tape, perpendicular to the other two pieces of Kapton as shown.
1.27mm pitch perfboard (for nozzle plate)
Kapton Tape
SiC Filament

## Slide 14
Installing the heating element
8. Secure the filament to the 1.27mm pitch perfboard nozzle plate and across the heater row with Kapton tape, perpendicular to the other two pieces of Kapton as shown.
1.27mm pitch perfboard (for nozzle plate)
Kapton Tape
SiC Filament

## Slide 15
Installing the backplane
9. Find your m1.2X3mm self tapping screws and precision screw driver…
Backplane fasteners

## Slide 16
Installing the backplane
9. Find your m1.2X3mm self tapping screws and precision screw driver…
Precision Philips screws driver magnetic bit
Back plane laid on top of the secured SiC fiber and nozzle plate
1.27mm perfboard for nozzle plate

## Slide 17
Installing the backplane
10. Lay your backplane gently across your now tapped down silicon carbide monofilament heating element, being sure to align every other hole in the nozzle plate, with each hole in the backplane, and extract a m1.2 X 3mm self tapping screw from the box.
Precision Philips screws driver magnetic bit
Back plane laid on top of the secured SiC fiber and nozzle plate
1.27mm perfboard for nozzle plate

## Slide 18
Installing the backplane
11. Firmly press and screw the m1.2 X 3mm screw into one one of the aligned holes, preferable one at the far left corner of the backplane closest to the edge. It should bite and screw in easily. Tighten it until it is firm and snug, and resists further turning. But no tighter.
Backplane
M1.2X3mm screw
1.27mm perfboard for nozzle plate
SiC fiber
Precision screw driver

## Slide 19
Installing the backplane
12. Repeat this fastening process, being careful to stagger the screws and install them adjacent to the heater row, so that no two are on the same column. This will make soldering easier later, and ensures a uniform clamping force on the heating element which provide consistent electrical and thermal contact.
2.54 mm perfboard Backplane
Staggered M1.2X3mm screws
1.27mm perfboard for nozzle plate
Precision screw driver

## Slide 20
Installing the backplane
12. Repeat this fastening process, being careful to stagger the screws so that no two are on the same column. This will make soldering easier later, and ensures a uniform clamping force on the heating element which provide consistent electrical and thermal contact.
2.54 mm perfboard Backplane
Staggered M1.2X3mm screws
1.27mm perfboard for nozzle plate
SiC fiber heater on heater row

## Slide 21
Installing the backplane
Line to probe along…
13. Set your multimeter to the 200 Ohm setting, and probe each pair of adjacent contacts along the heater row on the now secured backplane.
Go back and tighten the screws until all the heater resistances read between 10 and 100 ohms. If all your screws are tightened evenly, all the resistances should cluster between 20 and 50 ohms.

## Slide 22
Installing the backplane
13. Set your multimeter to the 200 Ohm setting, and probe each pair of adjacent contacts along the heater row on the now secured backplane.
Go back and tighten the screws until all the heater resistances read between 10 and 100 ohms. If all your screws are tightened evenly and sufficiently, all the resistances should cluster between 20 and 50 ohms.
2.54 mm perfboard Backplane
1.27mm perfboard for nozzle plate
Multimeter probes

## Slide 23
Releasing the printhead
14. You may now use your hack saw, or mill to carefully release the print head assembly from the nozzle plate stock, if you did not cut the nozzle plate out separately…
This will be done by cutting flat through the surface of the 1.27 mm perfboard stock as shown…
1.27mm perfboard for nozzle plate
Hacksaw
Nozzle Plate

## Slide 24
Releasing the printhead
1.27mm perfboard for nozzle plate
Hacksaw in flat cut position
Nozzle Plate
Saw Motion
14. You may now use your hack saw, or mill to carefully release the print head assembly from the nozzle plate stock, if you did not cut the nozzle plate out separately…
This will be done by cutting flat through the surface of the 1.27 mm perfboard stock as shown…

## Slide 25
Releasing the printhead
1.27mm perfboard for nozzle plate
Nozzle Plate
14. Cutting through the 1.27mm perfboard is quite tough. It takes some patience and a turdy work surface. A clamp or other work piece holder can help, though it is possible to perform the release entirely by hand.

## Slide 26
Releasing the printhead
1.27mm perfboard for nozzle plate
Nozzle Plate
14. You may find that pieces of the nozzle plate stock 1.27mm perfboard break off as you saw through it. Stop once you can see the 2.54 mm perfboard back plane showing. Be sure to leave the 2.54 mm perfboard excess material around the nozzle plate, to use as a flange for later.
Back plane flange showing

## Slide 27
Releasing the printhead
15. After perhaps 10 minutes of steady work, you should end up with something like what you see in this image of the released print head. Each active nozzle (every other hole in the 1.27 mm perfboard nozzle plate) is ~0.635 mm in diameter and ~1.6 mm deep. Each is plated with copper and nickel which serves as a thermal barrier coating.
Nozzle Plate
Back plane flange
Active Nozzles

## Slide 28
Releasing the printhead
15. Take note of the heater and nozzle locations. Each heater formed by the contacts of the 2.54 mm pitch perfboard pressing against the silicon carbide monofilament, create heaters that are cylindrical and have dimensions of ~0.5mm long X 0.135mm diameter.
Heater Locations
Back plane
Fastening screw